## Slide 1
- Evaluate prediction accuracy
- Correlation coefficient
- Normalized error %
- Peak error %
Motivation
- RC structures have complex behavior
- FEA status quo, analysis takes hours/days
- Deep learning (DL) successful in seismic response prediction
Algorithms of Interest
Methodology
Conclusion
- LSTM performed best: most consistent corr. coeff., lowest peak and norm. error
- Alg. performance is problem-dependent
- Data-driven methods learn from already seen responses
- LSTM and PhyLSTM better at predicting third floor response than roof
- PhyCNN better at predicting roof response than third floor
Acknowledgements
- Prof. Oral Buyukozturk (MIT)
- Prof. Kalil Erazo (Rice University)
- Prof. Ruiyang Zhang (SE University of China)
- Prof. Hao Sun (Renmin University of China)
References
Evaluation of Deep Learning Algorithms in Predicting
Seismic Response of a Reinforced Concrete Structure
Jacob Morgan¹, Oral Buyukozturk²
¹ Structural Mechanics and Design MEng Student , ² Professor of Civil and Environmental Engineering
Case Study: 6-Story RC Shear Wall Hotel
[1] Zhang et al. (2019). Computers & Structures, 220.
[2] Zhang et al. (2020). Engineering Structures, 215.
[3] Zhang et al. (2020). Computer Methods in Applied Mechanics and Engineering, 369.
Data-driven LSTM [1]
Physics-Informed CNN (PhyCNN) [2]
Physics-Informed LSTM (PhyLSTM) [3]
Trained with disp. time histories only
Trained with disp., vel., acc. time histories
Trained with disp., vel., acc. time histories
Task 1: Run the Algorithms With Original Study Data
Task 2: Acquire Earthquake Response Data
Task 3: Train and Test With New Data
Task 4: Compile and Evaluate Results
- Train with original data
- Verify code is running correctly
- Compare with original results
- Earthquake responses from:
- Ground floor
- 3rd floor
- Roof (7th floor)
- Data is processed and includes:
- Displacements
- Velocities
- Accelerations
- Variety of responses desired
- Retrain and test each DL model using same data
Output (Roof)
Output (Floor 3)
Input (Floor 1)
All three on GitHub with original data!
GitHub repository available via my profile:
https://github.com/jacobmorgan2023
https://github.com/zhry10
LSTM
(Long Short-Term Memory) Known for language prediction
How does architecture type and physics guidance affect prediction accuracy?
CNN
(Convolutional Neural Network)
Known for image classification
Training
Testing
?
?
Future Work
- Use true GPS/speedometer data - Use different architectures e.g. TCN
- Use shake table data (more instruments, documented damage)
Results
time
Δ
Δ
Δ
Algorithm-predicted responses of one event at one floor
Wide variety of training data characteristics to maximize performance
Correlation Coefficients
Test Quake 1 (High frequency, low PGA/PFA)
Test Quake 2 (Low frequency, high PGA/PFA)
High PGA/PFA: underestimated peak values
Low freq: better correlations
Peak Error Percentages (%)
Test Quake 2
Test Quake 1
Δ
Δ
Δ